## Slide 1: LAB Overview mbed Instructions for MultiTech mDot The Things Network/ARM/MultiTech

## Slide 2: Lab Overview
Labs
  Lab1: Setting up the system.
  Lab2: Getting Started with mDot EVB
  Lab3: Using mDot to send to The Things Network

## Slide 3: LAB 1 mbed Setup Instructions

## Slide 4: Lab Overview
Setup/Downloads
  Serial program
  mbed account
  Driver from ST
  Software downloads

## Slide 5: Serial Port Install Software
If you prefer Putty or another USB to serial solution please use it.
Install TeraTerm or similar Serial program.
http://ttssh2.sourceforge.jp/index.html.en
Click on the “download page”
Run “teraterm-4.87.exe” accept the defaults

## Slide 6: Windows Driver update
On https://developer.mbed.org/platforms/MTS-mDot-F411/
Slide down the page till “PC Configuration”
Click on “ST Link Driver” or use the below link https://developer.mbed.org/teams/st/wiki/ST-Link-Driver
“ST Link Driver” is now open.
Download “Download ST-Link/V2 driver”
Extract the zip file to a known location.
Depending on your machine, Run either dpinst_amd64.exe (for 64 bit system) or dpinst_x86.exe (for 32 bit). (As a reference: Window Button, Control Panel, System)

## Slide 7: Mac/Linux Serial Port
Mac and Linux Steps:
Follow the on line instrutions: https://developer.mbed.org/platforms/MTS-mDot-F411/

## Slide 8: Setup mbed Account and Add Platform
Go to developer.mbed.org
Sign-up and/or log-in (no instructions provided)
Add a Platform to mbed
(From www.mbed.org) Click on Developer(top), Platforms(top), MultiTech(Right side), Click on MultiTech mDot. Or Go to https://developer.mbed.org/platforms/MTS-mDot-F411/
Click on the blue box “Add to your mbed Compiler” (right side)

## Slide 9: Alternative Technique to add a Platform
In a Browser go to www.mbed.org
Click on “Developer Site”
Select “Compiler”
Click on (top right) “No Selected” or “Platform you already have setup”
Click “MultiTech mDot”(bottom) and “Select Platform” (top corner).
Bonus: you may add an additional platforms by clicking on “Add Platform”

## Slide 10: Processor Firmware Update (Missing Homework)
The following procedure can be used to update the CPU with new firmware.
Update your mDot board to the latest firmware https://developer.mbed.org/teams/ST/wiki/Nucleo-Firmware Web page “Nucleo Firmware”
Click on “Download the latest ST-LINK/V2-1 firmware upgrade”.
Download, Extract and Run “STSW-LINK007”
Plug the power to Developer board then USB cable.
Wait for USB Enumeration to finish. Click “Refresh device list”
Click “Open in update mode”
If needed, Click “Upgrade”. As of 2015/07/21 Version 11
After success Close the program.

## Slide 11: Starting code for mDot without EVB
Click on the Links and “Import this program” (Blue Box Right side).
Alt Tab to mbed Workspace . The computer is waiting for a program name to finish the install.
Click “Import” in mbed Workspace.
The Things Network Public LoRa Network mDot
https://developer.mbed.org/teams/The-Things-Network/code/mDot_Workshop/
Team Page
https://developer.mbed.org/teams/The-Things-Network

## Slide 12: LAB 2 Getting Started mDot EVB / The Things Network

## Slide 13: Lab Overview
Lab 2
  What do I have?
  Connecting to the network
  mDot-EVB Sensors

## Slide 15: Features and Descriptions
User Programmable LEDs
Two User Programmable Push Buttons, one reset
External Power Connector (remove the jumper)
JTAG SWD programming interface on MTDOT
Graphic LCD Display, optional backlight capability
USB 2.0 Micro B connector, “Full Speed”
Chip Antenna

## Slide 16: Sensors
Ambient Light Sensor: Intersil: ISL29011
Accelerometer: Freescale: MMA845x
Absolute Pressure and Temp: Freescale: MPL3115A2
I2C LED Driver: On Semi: NCP5623B
Display: LCD-Module: DOGS102

## Slide 17: mDot-EVB Block Diagram

## Slide 18: Power
Apply Power to mDOT-EVB from USB Port
Play …..
Attach grey cable, Insert micro UDK to USB
Wait.… Device drivers may take a period of time to load. A MULTITECH Drive should appear.
*** IF the drive is 20K, reseat the grey cable***
Select Configuration Mode on the EVB Menu
Red wire on the right
Pin 1 - Square Pad

## Slide 19: EVB - Connecting to The Things Network: AT Commands
Start Teraterm,
Click on Serial, Select Serial Port “XR21V1410 USB UART”,
Settings: Setup, Serial, values are: Baud rate: 115200(serial) Data: 8, Parity: N, Stop: 1,Flow: none. ECHO may need to be turned On (Terminal)
Type “AT” you should get an ok.
Type “?” you get a list of commands (try a full screen window)

## Slide 20: EVB - Connecting to The Things Network: AT Commands
Type “AT+FSB=7”
Type “AT+PN=1”
Type “AT+NI=0,???????”
Type “AT+NK=0,???????”
Type “AT&V”
Type “AT&W”
Type “ATZ”
Match the Conduit frequency settings
Enable Public Mode
Set APP EUI for The Things Network
Set APP KEY for The Things Network
Display the current configuration
Save the current configuration to flash
Reset the device

## Slide 21: LAB 3 mDot Sensors / The Things Network

## Slide 22: LAB 4: The Things Network
Tasks
Download the Program
Query sensor values
Send data to the network
Examine data on Cloud
Modify code for more sensor data and graphs.

## Slide 23: Starting Code
The Things Network Public LoRa Network mDot
https://developer.mbed.org/teams/The-Things-Network/code/mDot_Workshop/

## Slide 24: LAB Review Where to find/Is it repeatable/What do you need?

## Slide 25
MTDOT pin function mapping |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | Doc Rev 0.1 tab | 5/8/2015
mDOT Pin | 5V tolerant (1,2) | GPIO | SWD Interface | SPI Interface | I2C Interface | USARTs | Timer functions | RTC Functions | USB Interface | Event Trigger output | ADC Channels (3)
2 | Yes | PA2 |  |  |  | USART2_TX | TIM2_CH3, TIM5_CH3, TIM9_CH1 |  |  | EVENTOUT | ADC1_2
3 | Yes | PA3 |  |  |  | USART2_RX | TIM2_CH4, TIM5_CH4, TIM9_CH2 |  |  | EVENTOUT | ADC1_3
4 | Yes | PA6 |  | SPI1_MISO |  |  | TIM1_BKIN, TIM3_CH1 |  |  | EVENTOUT | ADC1_6
6 | Yes | PA8 |  |  | I2C3_SCL |  | MCO_1, TIM1_CH1 |  | USB_FS_SOF | EVENTOUT | 
7 | Yes | PC9 |  |  | I2C3_SDA |  | MCO_2, TIM3_CH4 |  |  | EVENTOUT | 
8 | Yes | PA12 |  |  |  | USART6_RX | TIM1_ETR |  | USB_FS_DP | EVENTOUT | 
9 | Yes | PA11 |  |  |  | USART6_TX | TIM1_CH4 |  | USB_FS_DM | EVENTOUT | 
11 | Yes | PA7 |  | SPI1_MOSI |  |  | TIM1_CH1N, TIM3_CH2 |  |  | EVENTOUT | ADC1_7
12 | No | PA0-WKUP |  |  |  | USART2_CTS | TIM2_CH1/TIM2_ET, TIM5_CH1, |  |  | EVENTOUT | ADC1_0
13 | Yes | PC13-ANTI_TAMP |  |  |  |  |  | RTC_AMP1, RTC_OUT, RTC_TS |  | EVENTOUT | 
15 | Yes | PC1 |  |  |  |  |  |  |  | EVENTOUT | ADC1_11
16 | Yes | PA1 |  |  |  | USART2_RTS | TIM2_CH2, TIM5_CH2 |  |  | EVENTOUT | ADC1_1
17 | No | PA4 |  | SPI1_NSS |  | USART2_CK |  |  |  | EVENTOUT | ADC1_4
18 | No | PA5 |  | SPI1_SCK |  |  | TIM2_CH1/TIM2_ET |  |  | EVENTOUT | ADC1_5
19 | Yes | PB0 |  |  |  |  | TIM1_CH2N, TIM3_CH3 |  |  | EVENTOUT | ADC1_8
20 | Yes | PB1 |  |  |  |  | TIM1_CH3N, TIM3_CH4, |  |  | EVENTOUT | ADC1_9
23 | Yes | PA14 | SWCLK |  |  |  |  |  |  | EVENTOUT | 
24 | Yes | PA13 | SWDIO |  |  |  |  |  |  | EVENTOUT | 
26 | Yes | PB3 | SWO | SPI1_SCK |  | USART1_RX | TIM2_CH2 |  |  | EVENTOUT | 
27 | Yes | PA10 |  |  |  | USART1_RX | TIM1_CH3 |  | USB_FS_ID | EVENTOUT | 
28 | Yes | PA9 |  |  | I2C3_SMBA | USART1_TX | TIM1_CH2 |  | USB_FS_VBUS | EVENTOUT |